## Slide 1
DEEPNAP SOFTECH · FOR JP MINDA GROUP
CNG Cylinder Process Tracking
Workflow Implementation Report
How every cylinder's 21-stage journey is captured, evaluated, stored and delivered — machine to dashboard.
CAPTURE
SAP · machines · operators push every stage event
EVALUATE
each reading checked against stage limits
DELIVER
live dashboards, trace & audit for every Pipe ID
July 2026 · digitization.jpmgroup.co.in

## Slide 2
THE WORKFLOW
One cylinder, 21 tracked stages
The exact manufacturing flow from your Process Flow document — every stage becomes a digital checkpoint.
1
Pipe Cutting
2
Bottom Spinning
3
Bottom Milling
4
Cyl. Sr. No. Marking
5
Neck Spinning
6
Heat Treatment
7
Hardness Testing
8
Neck Cutting
9
Neck Machining
10
Neck Threading
11
W/C & HST
12
Inside Cleaning
13
Air Leak Testing
14
Air Drier
15
Int. Shot Blasting
16
Ext. Shot Blasting
17
Ultrasonic Testing
18
Data Stamping
19
Painting
20
PAUT – Cyl. Bottom
21
Storage on Pallet
Forming
Heat & Machining
Clean & Test
Finish & Store
Stage 1 gives every cylinder its identity — the Pipe ID. Entered / scanned at Pipe Cutting, it travels through all 21 stages: every machine reading, result and timestamp is written against it. Stages 2–21 are machine-fed automatically.

## Slide 3
HOW IT WORKS
End-to-end: machine signal to live dashboard
1 · SOURCES
SAP S/4HANA
pushes stage data + Pipe ID
Machines / PLCs
push readings directly
Operators
scan-in & manual entry
2 · INGEST
Secure APIs
/sap/ingest · /cng/ingest
API-key auth
registered x-api-key
Always accepts
never blocks a machine
3 · PROCESS & STORE
Raw archive
payload kept verbatim
Normaliser
aliases → clean fields
SQL + Mongo
business + telemetry
4 · OUTPUT
Live dashboards
5 screens, real-time
KPIs & occupancy
computed per stage
Full trace
any Pipe ID, any time
Design rule: capture first, interpret second. The line never waits on software — data is accepted in any shape, archived raw, then normalised and evaluated.

## Slide 4
DATA ACQUISITION
Three ways stage data reaches the system
SAP push (primary)
Minda's SAP maps its data to our published format and POSTs one message per machine event — always carrying the Pipe ID, stage and readings.
POST /api/v1/sap/ingest
Machine / PLC push
Machines or edge gateways post JSON directly, exactly like the proven EKC & JCI telemetry lines already running on this platform.
POST /api/v1/cng/ingest
Operator entry
Stage 1 (Pipe Cutting) births the Pipe ID via manual entry / barcode scan; scan-in links a cylinder to a machine wherever needed.
Operator screen / scanner
ONE STAGE EVENT — THE MESSAGE
{
"machineId": "HT-401",
"stageNo": 6,
"pipeId": "JPM24C08921",
"ts": "2026-07-04T09:41:22Z",
"data": {
"furnace_temp": 892,
"soak_min": 42,
"result": "OK",
"status": "run"
}
}
pipeId on every message = traceability with no extra hardware.

## Slide 5
INGEST PHILOSOPHY
Accept everything. Archive raw. Then make it clean.
1 · ACCEPT
Any JSON shape is taken with a 2xx — single object, array batch, nested or flat. A schema change upstream never stops the line.
2 · ARCHIVE RAW
The exact payload is stored untouched (SAP inbox / telemetry store) — a permanent audit copy that can be re-processed anytime.
3 · NORMALISE
A tolerant mapper resolves field aliases (machineId / machine_id / device…), units and timestamps into one clean stage-event record.
4 · VALIDATE
PLC fault sentinels (-32768, 32767, 65535) are quarantined, duplicates dropped, and only clean values reach evaluation.
Why raw-first? Machine formats drift, SAP mappings evolve, vendors change firmware. Because the original payload is always kept, nothing is ever lost — history can be re-normalised under new rules without asking anyone to resend data.

## Slide 6
STAGE EVALUATION
Every reading judged against the stage's limits
1
Range check
Each parameter is compared to the stage's engineering window (min–max per metric — temperature, pressure, hardness, thickness…).
2
Stage result
The stage event is stamped OK or NG and written to the cylinder's permanent stage record with machine, time and values.
3
Defect capture
An NG result opens a defect entry — stage, machine, parameter and value — feeding the Defects board until closure.
4
Machine status
Every message also updates the machine's live state: run / idle / stopped / maintenance / fault, shown on the Machines wall.
AS SEEN ON THE DASHBOARD
Heat Treatment · HT-401
892 °C
window 850 – 950 °C → OK
Air Leak Test · ALT-1301
0.34 bar drop
limit ≤ 0.10 bar → NG · defect raised

## Slide 7
STORAGE
Two-tier storage: business truth + raw telemetry
SQL SERVER (JPMDO) — the business record
cng_cylinder — one row per Pipe ID — the cylinder master
cng_stage_record — one row per stage event: values, result, machine, time
cng_machine — live state per machine: status, latest gauges, ranges
cng_defect — every NG with stage, parameter and closure state
sap_inbox — raw SAP payload archive — full audit trail
cng_ingest_key — registered, hashed API keys per data source
Additive schema — new cng_* tables only. Existing Minda tables untouched, zero regression risk.
MONGODB — raw telemetry
Every machine packet, verbatim, as a time-series.
Loose schema by design — new sensors and fields appear without any migration.
Feeds re-processing, deep dives and future analytics (OEE, SPC, ML).
Why two tiers? Clean relational data gives fast, reliable dashboards; the raw archive guarantees nothing is ever lost. Each does what it's best at.

## Slide 8
COMPUTATION & OUTPUT
From stage records to live answers
Stage occupancy
cylinders currently sitting at each of the 21 stages — the live line-balance picture
WIP / completed
counts derived from each cylinder's furthest stage record — no manual tallies
Quality & defects
OK/NG rates per stage & machine; open defect ageing until closure
Machine liveness
latest reading vs range per gauge; stale feed detection via last-seen time
FIVE LIVE SCREENS
Live Ops
KPIs, occupancy, live event feed
Cylinder Trace
search a Pipe ID → its full 21-stage journey
Machines
machine wall with live gauges & status
History
filter any period, machine or stage
Defects
open NGs, ageing and closure
Real-time by design: Socket.io pushes an update the moment data lands; polling guarantees freshness even on flaky networks.

## Slide 9
TRACEABILITY
One Pipe ID — the complete life of a cylinder
BORN
Pipe Cutting (stage 1): Pipe ID created — scan or manual entry
TRAVELS
every SAP / machine message carries the Pipe ID with its readings
ACCUMULATES
up to 21 stage records: machine, values, result, timestamp
ANSWERS
search any Pipe ID → the full journey, seconds later, years later
1 Pipe ID
= 21 stage records, one audit trail
WHAT THIS UNLOCKS
Customer & IATF audits answered from a screen, not a paper hunt
Recall scope narrowed to exact cylinders, batches and machines
NG root-cause: see the same stage across every affected cylinder

## Slide 10
TECHNOLOGY
The stack behind it — and why each piece
Frontend React 19 + Vite + Tailwind
fast plant-floor dashboards; TanStack Query keeps data fresh
Backend Node.js · Express 5
one API layer for ingest, evaluation and dashboards
Business data SQL Server (Sequelize)
lives inside Minda's existing JPMDO — one platform, one login
Raw telemetry MongoDB time-series
schema-loose archive of every packet, ready to re-process
Real-time Socket.io + Redis
instant dashboard updates; cache & session backbone
Security JWT + x-api-key
role-based viewing; registered keys for every data source
SAP integration Push to our spec + OData
SAP maps to our format; material master synced from S/4HANA
Deployment Existing Minda infra
additive module on digitisationapi.jpmgroup.co.in · PM2

## Slide 11
SECURITY & GOVERNANCE
Locked down, auditable, zero-regression
Registered API keys
every pushing system gets its own key — stored hashed, revocable per source, no shared secrets
Role-based dashboards
viewing sits behind the existing Minda login (JWT) and role permissions — same accounts, same RBAC
Immutable raw audit
every inbound payload is archived verbatim with source & timestamp — a tamper-evident record of what was sent
Additive by design
only new cng_* tables; no foreign keys into and no changes to existing Minda tables — the platform you run today is untouched
HTTPS end-to-end
all traffic rides the hosted TLS domain; dev, test and production environments fully isolated

## Slide 12
WHERE WE ARE
Built, proven on live pushes — ready to scale to the line
DELIVERED & VERIFIED
Ingest APIs live — machine & SAP pushes verified end-to-end
Batch + single message formats, dividing into machine / cylinder / defect data
All 5 dashboard screens on real data, with live gauges & filters
16-machine demo line streaming (12 via SAP format + EKC/JCI patterns)
Published integration spec shared for SAP field mapping
NEXT — TO GO LIVE
SAP team maps live fields to the published format (sample + key already shared)
Production API keys issued per source system
Operator scan-in station at Pipe Cutting (stage 1)
Stage limit sign-off with quality team (min–max per parameter)
Go-live line by line, monitored against the raw archive
Deepnap Softech · deepnapsoftech@gmail.com · CNG Cylinder Process Tracking for JP Minda Group